## Slide 1
Institute for Energy, Environment and Sustainable Communities (IEESC)
University of Regina
Regina, Saskatchewan, Canada
Development of Climate Change Projections for Prairie Hydrological and Water Quality Modeling
(funded by the Canadian Water Network)
*Hua Zhang and Gordon Huang
The 4th NARCCAP Users’ Meeting, April 10-11, 2012, Boulder, CO.

## Slide 2
The Canadian Prairies
520,000 km2
Breadbasket
of Canada
Critical ecosystem services
<100 km2
Semi-arid climate
Snow-dominated hydrology
Agriculture
Sensitive to climate change

## Slide 3
Projection of Climate Change
Trends in impacts studies in prairie region…
GCM
Single RCM
RCM ensemble
Challenge #1
How to evaluate and combine RCMs?
Different time scales
Different statistical features
Precipitation occurrence

## Slide 4
Projection of Climate Change
Trends in impacts studies in prairie region…
GCM
Single RCM
RCM ensemble
Challenge #2
How to fit small prairie watersheds?
2500-km2 grid vs 100-km2 watershed
Statistical downscaling
Multiple weather series

## Slide 5
Framework
Weather
Generator
Site-scale validation/projection
Monthly shifts
Multiple weather series
Weighted
Ensemble
Multiple RCMs
Evaluation metrics
Weighting and projection
Watershed Simulation
Integrated simulation system
Uncertainty analysis
Risk analysis
Coupled Downscaling
Integrated Watershed Modeling

## Slide 6
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Metrics

## Slide 7
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Metrics
Interannual circulation pattern
Variability of annual temperature (SD):
Variability of annual precipitation (CV):
Linear trend of annual temperature (regression coefficient)
Linear trend of annual precipitation (regression coefficient)

## Slide 8
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Metrics
Seasonal circulation pattern
Correlation of seasonal temperature
Correlation of seasonal precipitation
Interconnection of seasonal temperature and precipitation

## Slide 9
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Metrics
PDFs of daily variables
Overlap of daily minimum temperature PDFs
Overlap of daily maximum temperature PDFs
Overlap of daily precipitation PDFs
(Perkins et al. 2007)

## Slide 10
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Metrics
Extreme events
99.7th of daily precipitation
0.03rd of daily minimum temperature
99.7th of daily maximum temperature

## Slide 11
Metrics for RCM Evaluation
M1
M2
M4
M5
M3
Precipitation Occurrence
Length of wet and dry spells
Occurrence of wet day (wet-wet: probability of a wet day following a wet day; wet-dry: probability of wet day following a dry day)
Metrics

## Slide 12
Combination of Metrics
Weights of RCMs:
???
Precipitation:
Ensemble-based projection:
Temperature:
Day | RCM1 (w=0.3) | RCM2 (w=0.4) | RCM3 (w=0.3) | ENS
D1 | 3 | 0 | 0 | 0.9
D2 | 0 | 5 | 3 | 2.9
D3 | 0 | 0 | 2 | 0.6
D4 | 3 | 4 | 0 | 2.1

## Slide 13
Combination of Metrics
Weights of RCMs:
Precipitation:
Day | RCM1 (w=0.3) | RCM2 (w=0.3) | RCM3 (w=0.4) | ENS
D1 | 3 | 0 | 0 | 0
D2 | 0 | 5 | 3 | 2.9
D3 | 0 | 0 | 2 | 0
D4 | 3 | 4 | 0 | 2.1
For example, W* = 0.5
Ensemble-based projection:
Temperature:

## Slide 14
LARS-WG
Developed by Semenov and Barrow (1997)
Alternate wet/dry series by monthly semi-empirical distributions
Daily values calculated by Fourier series and normal distribution
Using monthly shifts to reflect climate change (from the ensemble)
Stochastic Weather Generator (SWG)
SWG: reproduce observed climate normals, but not the actual sequences of single events

## Slide 15
New Willows
Old Willows
New Willows
Old Willows
New Willows
Old Willows
Study Area
The Assiniboia Watershed
Area: 49.7 km2
Elevation: 693 -773 m
Land use: farming
Soil: Chenozemics
Annual T: 3.9ﾟC
Annual P: 393 mm
Annual PET: 1135 mm

## Slide 16
Data Collection
RCMs
CRCM, OURANOS, Canada (DAI & NARCCAP)
HRM3, Hadley Centre, UK (NARCCAP)
RCM3, UC Santa Cruz, US (NARCCAP)
WRFG, PNNL, US (NARCCAP)
Projection
Baseline: 1971–2000
Future: 2041–2070 (A2)
Models: CGCM3/CRCM, HadCM3/HRM3, CCSM/WRFG, GFDL/RCM3
Validation
Driving data: NCEP II (1974-2003)
Observation data: Canada 10-km gridded dataset (1961–2003), produced by AAFC & NRC

## Slide 17
Results: Evaluation of RCMs and Ensemble

## Slide 18
Projection of Climate Change (by ensemble)
Climate Change Predicted
Month | Tmin* | Tmax* | Tstd** | Precip** | Wet Spell** | Dry Spell**
Jan | 4.91 | 3.88 | 0.15 | 0.36 | 0.27 | -0.27
Feb | 2.66 | 2.06 | -0.06 | 0.24 | -0.05 | -0.09
Mar | 2.32 | 2.15 | -0.20 | -0.15 | 0.09 | 0.23
Apr | 2.31 | 2.58 | -0.35 | 0.22 | 0.00 | -0.04
May | 1.90 | 1.40 | -0.38 | 0.20 | 0.21 | 0.01
Jun | 3.29 | 1.69 | -0.08 | -0.01 | -0.04 | 0.28
Jul | 3.66 | 1.73 | -0.20 | 0.03 | -0.07 | -0.17
Aug | 4.04 | 1.30 | 0.01 | 0.79 | 0.04 | -0.19
Sep | 3.09 | 2.88 | -0.26 | -0.29 | -0.11 | 0.02
Oct | 2.88 | 2.60 | -0.25 | -0.08 | 0.02 | 0.01
Nov | 3.47 | 3.12 | 0.27 | -0.24 | -0.01 | 0.26
Dec | 2.36 | 1.53 | 0.02 | -0.04 | -0.04 | 0.13
Annual | 3.07 | 2.24 | -0.11 | 0.09 | 0.03 | 0.01
Note: * absolute change; ** relative change.

## Slide 19
Results: Validation of LARS-WG
Climate Change Predicted

## Slide 20
Results: Projection of Climate Change
Climate Change Predicted

## Slide 21
RCM performance
Warm bias in winter temperature
Dry bias in summer rainfall
Misinterpretation of prairie landscape (small wetlands)
Further improvement
Weighting scheme (threshold of precipitation occurrence; multicriteria assessment)
Sample size (models and scenarios)
Multi-site weather generator
Discussion

## Slide 22
Surface data (topography, bathymetry, soil, land use, etc.)
Hydrological module
Biochemical module
N Cycle
P Cycle
DO
Balance
Phyto.
Kinetics
Hydrodynamic module
Thermal module
Overland
Flow (Q, T)
Lateral
Flow (Q, T)
Channel
Flow (Q, T)
Point Loading (N, P, DO, BOD)
Diffusive Loading (N, P, DO, BOD)
Vel, Depth
Water T
Meteorological data (Tmp, Wind, Hum, Rad, Precip, Cloud, etc.)
Water Use
Watershed Model
Hydrodynamic Model
Eutrophication Model
Multi-level Watershed-reservoir Modeling System (MWRMS)

## Slide 23
Metereological Data
49.61° N, 105.87° W, Vantage Pro2-6162
Temperature, precipitation,
wind direction & speed, humidity, radiation, pressure
(Daily or 30-min)
2009-2010
49.73° N, 105.95° W, STN# 4020286
1960-2010

## Slide 24
Hydrolocial Data
Assiniboia water plant station: weekly water level, 1978 - 2010
PFRA station: daily inflow rate, 1976 – 2003
Automatic water logger (WL16)
Water level & temperature (30-min)
2009 - 2011

## Slide 25
Water Quality Data
Automatic monitoring
DO, turbidity, BGA, Chlα, pH, temperature, water depth
per 30-min, 2009 – 2010
Sampling & lab analysis
NO3-N, NH4-N, TKN, SP, TP, BOD, Chlα, Ortho-P
wkly/mthly, 2008 – 2010

## Slide 26
Calibration Results: Watershed Hydrology
Calibration
Validation
Calibration:
NS = 0.83
PBIAS = 0.41
Validation:
NS =0.95
PBIAS = 10.83

## Slide 27
Calibration Results: Reservoir Water Quality
Site: OWR-S5
Depth: 0.5 m
Time: 2009 – 2010
Simulation
Observation

## Slide 28
Hydrological Response to Climate Change ChangeHydrometeorological Changes
Snow/Total P
ET
ET/PET
Water Yield
Less snow; increased ET; decreased water yield

## Slide 29
Biogeochemical Responses to Climate Change
More nutrient loss; degraded water quality (eutrophication)

## Slide 30
Related Publications
Climate Change Predicted
Zhang, H., Huang, G.H., Wang, D.L., et al.. An integrated multi-level watershed-reservoir modeling system for examining hydrological and biogeochemical processes in small prairie watersheds. Water Research, 46(4): 1207-1224.
Zhang, H. and Huang, G.H. (2009). Building channel networks for flat regions in digital elevation models. Hydrological Processes, 23(20): 2879-2887.
Zhang, H., Huang, G.H., Wang, D.L. and Zhang, X.D. (2011). Uncertainty assessment of climate change impacts on the hydrology of small prairie wetlands. Journal of Hydrology, 396(1-2): 94-103.
Zhang, H., Huang, G.H., Wang, D.L. and Zhang, X.D. (2011). Multi-period calibration of a semi-distributed hydrological model based on hydroclimatic clustering. Advances in Water Resources, 34: 1293-1303.
Zhang, H. and Huang, G.H. Development of climate change projections for small prairie watersheds using a weighted multi-RCM ensemble and a stochastic weather generator. Climate Dynamics.
Zhang, H. and Huang, G.H. An integrated stochastic-fuzzy modeling approach for risk assessment of soil water deficit and reservoir water quality degradation under climate change. Science of the Total Environment.
Published:
Under Review:

## Slide 31
Coupled downscaling: Ensemble + SWG
Enhanced confidence
Increased resolution
Improved efficiency
Better connection with watershed hydrological and biogeochemical modeling
Better support for impact studies in small prairie watersheds
Summary

## Slide 32
Recommendations to NARCCAP
Climate Change Predicted
Distribute biweekly or monthly newsletters
Provide online training courses for data analysis and management
Organize online meetings (skype) for small group discussions

## Slide 33
Thank You Very Much
Notes: That’s all. Thank you very much!